Oreilly – Java Concurrency

---
Hardware
- Concurrency
  - Performance – Efficient use of resources
  - GUI – Illusion of always performance
- Log Linear – Exponential Growth
- A Scary Graph – To the Right
  - We added more Transistors but
    - clock speeds have plateaued
    - Need more wats so generating more heat so need better cooling system
      - Heat gets to hight could melt the silicon chips
    - Boot out at 18 instructions
- What happens to overall performance as the increase CPU Performance decreases
  - software optimization become more important
- Speed Memory
  - 1980 – Took the same time to do a multiplication as access memory
  - Takes a 1000 time long to achieve data than to operate one it

---
Hardware
  - We get stalled waiting for data -- The processor is idle. ( Use Picture from previous page )
    - How to improve
      - Could make our CPUs multicore
      - Could add Caches
  - Scary Clown
    - We have two cores with L1, L2 and L3 Caches, A Northbridge (bus) and memory
    - Adding cache is where we get the performance back using multicore
    - L1, L2, L3 Cache are all the same ( 6 transistors in a pattern – get one bit of cache )
      - L1, L2 are private and L3 is shared between cores.
      - Ex. 1 Meg of Cache is 48 million transistor
        - Need the transistors for other such as processing cores
      - Why is there so little cache
        - Number of Transistors
        - Arrangement – How far the cache is away from the
          cores determine the speed of the cache
        - Geometry – Go further away bigger ( more space ) ,
          close to the CPU core less space
    - Speed of the North Bridge
    - So now the processor can gets it data from L1, L2, L3 or from memory using the North Bridge
    - Rule of Thumb
      - Registers – No Waiting
      - 4 clock Cycles L1 and 167 clock cycles L2, 300 to 400 for main memory

---
Demo -- Caching
- Prerequisites
  - TouchEveryLine, TouchEveryItem first to make sure there is no JIT Compilation or other weirdness
  - Using primitives to avoid garbage collection effects and object allocation
- When doing performance measurements remember Java is a noisy language
  - number within 10% should be the same
  - performance – Run on machines that have only as much needed to perform the tests
- Results
  - When touchEveryLine is doing every eighth vs all. Why does it take the same amount of time?
    - Vast Majority of the work is moving data backwards and forwards through the Northbridge from main memory
    - Done in chunks of one whole cache line
      - The real work is dominated by the transfer time of to and from main memory
  - When considering times it is not only your work, but the JVM, the hardware and timings

---
Need for Syncrhonization
- 2 processes or 2 cores or 2 threads are trying to access the same data –
  core of why we need synchronization
- Strong or weak memory model
  - Java has a weak memory model
  - Defined by the MESI protocol ( Modified, Exclusive, shared, invalid)
    - At the hardware level
    - approach to how hardware wants to share memory in a consistent or
      inconsistent way
    - The Java Model of synchronization will be built on top of MESI

---
Fundamental Concepts of Java Concurrency
- Fundamentals
  - shared – visible by default mutable state
    - All Java threads live in the same process
    - The Same process shares the same heap ( The heap is always visible by all the threads )
      - and no software protections from being modified
    - How do you coordinate them
  - preemptive thread scheduling ( Each thread gets a certain amount of time to run )
    - Java Threads are Operating Threads
    - They are managed and scheduled by the OS
    - The OS does not communicate with the User Thread in any way.
      - Threads get started and stop by the OS
      - The thread may not be finished updating when it is stopped
    - What happens when a thread is swapped off a core?
      - Thread is suspended immediately
      - It may be in an inconsistent state
  - Objects must be locked to product vulnerable state
    - A mechanism to say this object is not available and some other process is busy with it
    - Even reading the thread could provide incorrect information

---
Java Concurrency Model
- To protect against inconsistency, need to use exclusion
  - only available mechanism
  - synchronized key word which must be opt into
- All code using share mutable state inconsistent must cooperate
  - Modifies or reads
  - Code which does this is concurrently safe
  - Ex. Five different classes which are using shared mutual state and every method that touches the shared mutual state must have synchronized box or methods

---
Objects must be locked to Protect Vulnerable State
- Basis of intrinsic concurrency approach
- A Java Thread is an OS thread
  - Thread.start() calls the OS to clone() a new thread which is the owner of thread
- java.lang.Thread is just a metadata object
- OS Monitors used to awake threads
  - When a synchronized block/method is hit then if the object is not available we sleep and when the object is found the OS alerts the java program
- The OS does a lot:
  - Creating Threads
  - Putting Threads to sleep
  - Waking Threads up

---
Java Concurrency Model
- What does synchronized do
  - At a hardware level synchronizing main memory and caches.
    - Main Memory Representation of object being locked.
    - Happy Path
      - Blue locks the thread
      - Copies the data from main memory into cache
      - Does the operations and writes to main memory then release the lock.
    - Unhappy Path
      - Get Swapped Out
      - Write Back to main memory and hold the lock
    - Read from memory at start and write to memory at end of block.
    - Either acquire a lock or fail to acquire a lock ( in which case you block until it becomes free )
  - Exclusive ownership of an object
    - When a synchronized lock is acquired the current thread owns the object
    - modify an object’s shareable state – Indication of temporary exclusive access to the object.
      - acquire object’s monitor ( stored in object header )
  - Critical Section – Only one thread at a time is allowed into this critical section of code.
    - An object can inconsistent for period of time when synchronized

---
Volatile
- provides exclusive access to data by synchronizing the cache of one thread with the main memory representation
  - It provides critical section behavior
  - Provides 1 operation to or from main memory
    - No locking is involved
    - Caches are flushed.
  - When a field is declared volatile – Before using this variable with reading or writing ignore what is in the caches
    - Read a volatile variable then discard current value in the cache and read directly from main memory
    - Write a volatile variable put the value in the cache and flush it to memory
  - Volatile variables cannot be used for state dependent updates
    - Can’t do v++ with volatile, but use a synchronized block ( 2 operations since v appear on the right and left hand side )
    - not safe for state dependent updates
  - Volatile cannot cause deadlocks since they have no locks
- Java Concurrency is protect vulnerable mutable data ( it is about the data and not the objects )
- Good Use -- Example a flag within a multi-thread operation
  - can help ensure the visibility aspect of the data change without providing mutual exclusion.

---
Demo -- Synchronization
- Why don’t we synchronize every method on Java
  - Unsafe = 5 second	50% loss
  - Synchronized = 504 second	0% loss
  - Volatile	= 277	50% loss
  - AtomicCounter() = 279	0% loss
  - Difference is an order of magnitude 2
- synchronized(this)

---
Fun with Counters
- Stack Machine
- First Picture is a Single Thread Program which works fine
- Second Picture is a Multithreaded Program
  - A context switch happens at process 8.
    - I was changed and it is still sitting in thread A’s private stack and not the heap.
    - When Thread B read the memory it gets the original value of I
  - Synchronized
    - bytecode operations: monitorrenter, monitorexit – Start and End of Thread
      Context
      - monitor exit can also be used in exception handling
- Synchronized – See doc/synchronzied.bc
  - bytecode operations: monitorrenter, monitorexit – Start and End of Thread
    Context
    - monitor exit can also be used in exception handling
    - Load the Objects from the Heap Storage, but the value is still on the stack

---
Thread LifeCycle
- Timeslice is usually 10 millisecond
- States
  - Sleep is well defined amount of time or else it goes back to start
  - Waiting is an indefinite amount of time
    - Done by UNIX Signals

---
Thread Class
- Lightweight unit of execution
  - Smaller than a process capable of executing java arbitrary code
- Each thread is a full unit of execution to the OS
  - Own Stack frames ( belong to each individual thread ) and Program Counter
  - Main address heap shared between all thread in the process
  - Its scheduled
- When a method is entered a new stack is located on it to keep temporaries ( evaluation stack )
- Thread States
  - New – Thread is created, but have not been scheduled
  - Runnable – the thread is running or available to run, but the OS schedules the thread
    - Running and Available change so fast it is good to put them into the same state
  - Blocked – The thread is not running, but is waiting to acquire a lock or in a system call
  - Waiting – The thread is not running but has been called by Object.wait() or join
  - Timed_Waiting – The Thread is not running it has called object.wait() or Thread.sleep() -- Dependent on timed waiting
  - Terminated – Thread has terminated either successful or threw an exception

---
Thread Class
- Methods
  - getId(), setName(), getName(), setState(), isAlive(), start(), interrupt(), isInterrupt(), join()
    - join – Current thread pauses and wait for other thread to exit
    - When the isInterrupt has been called or it is in the exception the interrupt flag has been cleared.
  - getPriority(), setPriority(), setDaemon(), setUncaughtExceptionHandler()
- 2 Types of thread
  - daemon thread
  - system thread
- UncaughtExceptionHandler() -- Run on the handled thread, not the current thread
- Never use
  - Stop -- Almost impossible to use without violating safety
  - Suspend, resume, countStackFrames
    - Does not release any monitors – deadlocks
  - Destroy – Never Implemented would have suffered the same problems as suspend. ( stop at 130 minutes)

---
Java Memory Model
- What happens when two cores access the same memory model
- var handles expands beyond normal access and volatile access
  - Fill in later
- Questions that the memory model answers
  - What happens when two cores access same data?
  - When are they guaranteed to see the same value?
  - How do memory caches affect this?
  - Cache coherency protocols (MESI)
- Two possible approaches
  - Must code to the JMM not the hardware.
    - Intel is much stricter than ARM that it might uncover bug when moved to an ARM processor
  - Strong Memory Model ( all cores see the same values )
    - requires more implementation code on top of weak hardware
    - Scales worse as the number of cores increases
    - Cache Invalidation swamps the memory bus
      - The throughput from Northbridge going to 0 since so much time would be keeping the memory model consistent
  - Weak Memory Model ( special cache instructions ) -- Used by Java
    - Fits in better trend in processes
    - Make porting easier

---
Java Memory Model
- Mathematical Description of how Memory works and Most impenetrable part of JLS
- JMM makes minimal guarantees – Real JVMS and CPUs may do more
- Key Concepts ( low level basic set of rules )
  - Happens Before
    - One block completes before other can start
    - synchronizes blocks
  - Synchronizes with
    - Action will synchronize its view of an object with main memory
    - synchronizes with another block at that point
    - Volatile is just a synchronize with
    - Threads have their own description of an object’s state – must be flushed to main memory and other threads
    - synchronized meas the local view has been synchronized with other threads
    - Define touch points where threads must perform syncing
  - As-if Serial
    - Instructions appear to execute in order
    - Looking as an outside thread means that the instructions will execute in order – Inside the thread the instructions can be order in any way.
  - Release-Before-Require
    - lock release before another thread requires it
- Synchronize Blocks are a combination of happens before and synchronizes with primitives
- volatile is a synchronizes with

---
Summary
- Unsynchronized methods – Don’t care about the state of locks and can run while other methods are running
- only objects can be locked not primitives
  - primitives are collection of bytes, don’t have an object header such as an class
  - can be immutable, but has a header that cannot be changed
  - arrays are objects
  - For an array must lock the object and the internal values of the outside
- Locking an Object[] does not lock the individual objects
- A synchronized method is equivalent to a synchronized (this) { ... } block that covers the entire method
- Synchronization of an inner class is independent of the outer class
- When locking class objects two options
  - explicit lock on class liter using getClass()
  - Both approaches have different behavior in subclasses
- Synchronized is not part of the method signature it can not appear on a method declaration of the interface
- Java locks are reentrant – A recursive call to to synchronized methods will not self dead lock

---
Deferred Executions
- A class is the smallest unit of functionality
  - Functionality is loaded and linked as classes
  - Must go through class loading
- Java has no free functions
- Tasks to be executed is represented as an object
  - instance of some interface
- Representing execution means were deferring execution
  - Have a reference to some code which will be executed later
  - Callable – Here is some code run it and when call is return then the return value is returned
  - Supplier – Use the value when you get when you run this bit of code
  - Runnable – Start this code in a different thread via a Thread Constructor
  - Callbacks – Here is some code – Call it back when something happens (ex. setExceptionHandler)
- Deferring Execution comes up in other contexts
  - closures / Lambda Expressions / Function Pointers
  - Specialist Task Libraries
  - Futures from Java.util.concurrent

---
Executors in Java.util.conconcurrent
- Executors are java’s standard thread pools
- Accepts Tasks and execute them on a different thread
  - The tasks expects a Runnable Interface
- Does not block the thread providing the task
  - Pattern : Here is the task and hand it to another thread and the main thread carries on
- Tasks may queue if not execution thread is immediately available
  - Executors often incorporate a blocking queue
- Base interface is Executor Services which is a subinterface of Executor
  - ExecutorService Interface is subinterface of Executor

---
Executors – Stop at 153
- java.util.concurrent has factories for making thread pools
  - in the Executors Class has a bunch of factories produce customized ThreadPools
  - ThreadPools – If you have a thread available it starts are you wait until one becomes free.
    - Don;t have to pay the cost of thread creation each time
    - Must be able to prove that the task you send it terminates in bounded time or the task from the threadpool will never be returned
      - decreases throught put
      - Tasks could get loss if shutdown with a queue that is not empty.
      - For rate limiting us an rate limiting queue. (153)
  - ThreadPoolExecutor is a bas class which is instantiate and general purpose
    - Best Practice use what in Executors
    - Ready Made ThreadPools – All Based on ThreadPoolExecutor
      - newFixedThreadPool(int nThreads)
      - newSingleThreadExecutor()
      - newCachedThreadPool()
      - newScheduledThreadPool()
  - If you are not using java.util.concurrent then you end up reimplementing half the classses in it
  - product ExecutorService instances
  - Example ScheduledExecutorService stpe = Executors.newScheduledThreadPool(2);

---
Fixed Size Thread Pool
Single Thread Executor
- Threads will be reused to run multiple programs
- Prevents having to pay the cost of thread creation
- If threads are used new tasks are stored in a queue
- Useful if tasks flow is stable and known
- Threads are only released when a task is completed
- Tasks must provably terminate in bounded time
  - A task with an infinite loop could steal a thread
- Single Thread Executor
  - Backed by a single thread
  - New submitted tasks are queued until the thread is available
  - Can be useful to control number of tasks concurrently executed
  - Also useful for testing – See things more easily
  - Essentially a special case for fixed pool

---
CachedThreadPool
- Cached Thread Pool
  - Will Create new Threads as required and reuse threads where possible rather than queue
  - Created threads are kept for 60 seconds after which they are removed from cache
  - Can give better performance with small asynchronous tasks or bursty workloads
    - Useful where you can’t control the rate which new tasks come in.
  - Potentially higher thread creation overhead
    - Could be a tradeoff vs Fixed Pool and just made it larger
  - More complex caching pools exit – Tomcat
    - Has a high and a low watermark
    - As long as the number of threads is between a high and low

---
ScheduledThreadPoolExuector
- Common choice of thread pool for many applications
  - ScheudledExecutorSerivce stpe = Executors.newScheduledThreadPool(poolSize);
- Scheduled Events can execute at a fixed rate
  - stpe.schedueAtFixedRate(msgReader, initialDelay, period, TimeUnit.MILLISECONDS)
- ScheduledExecutorService ( subtype of executorService ) returns a scheduled for pending execution
  - Allows cancellation
- Good for Control Concurrency Work

---
Scheduled Thread Pool Executor
- Want to schedule repeated events
- Returns a ScheduledExecutor Service and instead of returning a future it returns a scheduled future for things
  - stpe.invokeAll()
    - Executes a bunch of tasks at once
    - Returns a collection of Future Objects
    - Can be beneficial when you have sufficient hardware
- The Schedule Future can cancel pending tasks
- Can execute more than one task at once
- For Thread Pools can have shutDown and ShutDownNow() -- Correct way ( volatile shutdown )
  - ShutDown -- Basic idea is finished what you are doing, but don’t start any new tasks
  - ShutDownNow – Cancel the tasks you already have
  - Graceful Shutdown

---
Locks (Synchronized) Revisited -- Drawbacks
- There is only one type of lock ( Think he is talking about synchronization )
- Applies equally to all synchronized operations on locked objects
- Locks are acquired at the start of synchronized block or method
- Lock release at the end of block or method
- Locks are either acquired or the thread blocks – No other possible outcome
- Can imagine more general classes of locks
  - Different Types of blocks – Readers/Writers Block where writers can block
  - No restrict lock to block
    - Allow a lock in one method and unlock in another
      - Ex. Traverse down the getting different objects and locking the last two – Hand over Hand Locking
  - Could have a thread acquire a lock and fail or wait a period of time and then fial

---
Lock
- The main interface is java.util.concurrent.locks.Lock
- Methods
  - lock()	Acquires the lock
  - newCondition	Create a condition for wait/notify – Wait for something to change about the object
  - tryLock	Acquires a lock in a certain time
  - unlock	release the lock
- Instead of having the header of a class we will have a genuine object
- use lock instead of synchronized keyword
- Two Main Implementations
  - ReentrantLock	replicates the synchronized lock
  - ReentrantReadWriteLock	used for reader/writeLocks

---
Condition
- Intrinsic Concurrency only has 1 condition to wait on
- Lock.newCondition() creates a Condition Variable
  - Multiple Conditions can be created on a lock
  - No semantic meaning as in intrinsic concurrency
- Example – A reader does not have any data to consume
  - public class ReentrantLockWithCondition {
    - Stack<String> stack = new Stack<>(); int CAPACITY = 5; ReentrantLock lock = new ReentrantLock(); Condition stackEmptyCondition = lock.newCondition(); Condition stackFullCondition = lock.newCondition();
    - public void pushToStack(String item){
      - try {
        - lock.lock();
        - while(stack.size() == CAPACITY) { stackFullCondition.await(); }	// Done because every time it wake it must do the same check
        - stack.push(item);
        - stackEmptyCondition.signalAll();
        - } finally { lock.unlock(); } }
    - public String popFromStack() {
      - try {
        - lock.lock();
        - while(stack.size() == 0) {
          - stackEmptyCondition.await();	// Suspends the Running thread and release the lock – IllegalMonitor
      - }
        - return stack.pop(); }
      - finally {
        - stackFullCondition.signalAll(); . 	// If there are any threads waiting on the notEmpty condition, they'll all wake up. Then they'll contend for acquiring the lock
        - lock.unlock(); } } }

---
Atomics
Atomics Long
- java.util.concurrent provides Atomics
  - Guaranteed thread safe
  - No Missed Values
  - Faster than synchronized
  - cannot deadlock using an atomic
  - Change the value all other threads immediately see the update
- Atomics Integer and Long
  - Can be used as Counters
  - State Dependent updates
  - Replacement of Volatiles
    - reading an atomic performing a volatile read
    - writing an atomic performing a volatile write
    - increment – The reading and writing is the most expensive is done as a volatile
    - Based on atomic CPU Operations
  - Atomic Reference good for changing variables that are immutable or used by many threads
  - Composite Operations – Not defined in the Java Memory Model

---
Adders
Accumulators
- Atomic Long and Adders – As number of threads increases the performance worsens
  - Longer Adder is meant to solve this problem
  - LongAdder, Long Accumulator – Allows you take a double and have them like long
- Accumulators
  - Generalization of Adders
  - Accumulators are just new DoubleAccumulator((x,y)→ x + y , 0.0)
  - Same Contention as Adders

---
Atomic Reference
- Atomic Reference – Software Transactional memory Subsystem – Approach to handle a guarantee ( define data and state to be private to thread )
- Basic for Optimistic Transaction API
  - Clojure Software Transactional Memlory
- Atomic Functional Programming
  - Have an atomic reference
  - optimistically apply the application or aggregation
    - Function must be pure
  - succeed update the reference
  - Atomic Function Application and Aggregation

---
Concurrent Hash Map
- Don’t have to synchronize the whole structure, but on a per bucket basis
- Improvements
  - Java 7
    - Simple Segmented model
    - One Reentrant Lock object per hash bucket
    - Memory Intensive : size of Hash map + 16 * size of Reentrant Lock
  - Java 8
    - Once the Hash Chain crosses the threshold it changes from a link list to a balanced tree
    - Improves Worst Performance from O(n) to O(log n)-- The case for high collisions
- New Methods
  - compute
  - computeIfAbsent
  - forEach
  - getOrDefault
  - PutIfAbsent
  - remove
  - replace
  - replaceAll

---
Array List 225
- Less suitable for concurrent algorithms
  - hashmap are more spread and easier to be made concurrent
- Versioned Iterator – Have multiple thread that need a locally consistent view of the array
- Concurrent is a drop in replacement for a hashmap
- Collections.synchronized list – lot poorer performance
  - want to use a sequential data structure that is consistent
  - Will not throw ConcurrentModificationException
- Used a version data model
- CopyOnWriteArraySet – More efficient, but use when transversal outnumbers mutations by a lot